## Slide 1
2016 Ohio GIS Conference
September 28 - 30, 2016 | Hyatt Regency Columbus| Columbus, Ohio
A New Generation of Agriculture: The Rise of GIS and Precision Farming, an Ohio Case Study
Alexandria Horne
Farm Manager Horne Family Farms
Senior Computer Programming Analyst Cincinnati Area Geographic Information System (CAGIS)

## Slide 2
Introduction to precision farming
Case Study: fertilizer prescription map creation
USDA Open Data Portal
ArcMap Demonstration
Presentation Outline

## Slide 3: An approach to farm management that uses technology to ensure that crops and soil receive exactly what they need for optimum health and productivity.
Data Collection
Farming
Management Decisions
Analysis
What is Precision Farming/Agriculture?

## Slide 4
The goal is to ensure profitability, sustainability and environmental conservation
“A smorgasbord of technologies”
Global Positioning Systems
Geographic Information Systems
Direct & Remote Sensing
Variable Rate Technology
Real-time Monitoring
Precision Navigation

## Slide 6
Precision Operation Example

## Slide 8
Case Study – Horne Family Farms
- Family-run farm located just outside of Springfield, Ohio
500 arable acres
Corn (field)--cover--soybean rotation system
Conservation tillage system (Spring only disk pass)

## Slide 9
How VRT Works

## Slide 10
Variable Rate Technology (VRT)

## Slide 11
Fertilizer Prescription Map Creation
Resources used ArcMap 10.3 Garmin handheld GPS unit (Basecamp software) Google Earth USDA Web Soil Survey
GIS based input into VRT system software
Tells nozzles when/where to spray and at what rate/coverage
2 maps: Phosphorous (P)
Potassium (K)

## Slide 12
Steps to create prescription maps
Determine soil sample locations (grid based)
Take soils samples at designated locations
Send to lab for analysis
Input soil sample results (point attributes)
Calculate needed fertilizer rates (raster prescription maps)
Convert raster into classified polygon layer then export data
Load this data into precision equipped tractor for VRT application

## Slide 13
Field Boundaries (ArcMap)

## Slide 14
Creating a systematic soil sampling grid

## Slide 15
Completed soil sample grid based map

## Slide 16
Input soil sample results

## Slide 17
Interpolating soil sampling data
Ordinary Kriging (Geostatistical Analyst )

## Slide 18
Developing a phosphorus fertilizer prescription map

## Slide 19
Phosphorous Prescription Map

## Slide 20
Potassium Prescription Map

## Slide 21
Crop Spec software

## Slide 23
USDA Web Soil Survey
http://websoilsurvey.sc.egov.usda.gov/App/WebSoilSurvey.aspx
Specify an area of interest (AOI) polygon and examine the soil properties of that AOI

## Slide 24
Soil Taxonomy Classification of AOI

## Slide 26
Download data for integration into ArcMap

## Slide 27
Soil Drainage Behavior of AOI

## Slide 28
Soil Erosion Potential of AOI

## Slide 29
ArcMap Demonstration

## Slide 30
Thank you for your time! Are there any questions?
Alexandria Horne
alexandria.horne@cincinnati-oh.gov horne.alexandria@gmail.com